## Slide 1: Integrating Thorlabs Device in MATLAB
Wolfgang Skopalik

## Slide 2: MATLAB Overview

## Slide 3: Different ways
There are different ways to integrate devices in MATLAB:
Driver files (.dll, .lib): CCSx, WFSx
SCPI commands: PM100x, PM200, PM320E
Serial COM commands: DCx LED driver
For these devices sample codes are available.
In MATLAB generally low-level commands are easier to use.
But for some devices the driver files are the only way.

## Slide 4: General approach
The general approach is similar for each of these ways:
Get connection to the device
Perform measurement / switching / read out
Close connection to the device in the end

## Slide 5: Driver files
To use driver files in MATLAB, in most cases the header file „visatype.h“ has to be modified like this:
Comment out the calling conventions for 64-bit systems.
MATLAB / Compiler doesn‘t support them and returns an error message.

## Slide 6: Driver files
Sample code for CCS:
Loading the library into MATLAB
Show functions in the driver
Initialize the device with correct instrument ID

## Slide 7: Driver files
Pointers in MATLAB:
All of our drivers use pointers in some functions
In MATLAB pointers are created by „libpointer“
Correct „libpointer“ type can be seen in „libfunctionsview“

## Slide 8: Driver files
Sample code for CCS:
Set integration time and make a scan
Show the scan data
Close the connection to the device

## Slide 9: SCPI commands
For SCPI commands the VISA interface has to be installed

## Slide 10: SCPI commands
For SCPI commands the VISA interface has to be installed

## Slide 11: SCPI commands
For SCPI commands the VISA interface has to be installed
Resource name of device

## Slide 12: SCPI commands
Sample code for PM100A:
Set correct resource name
Open VISA session
Set connection parameters

## Slide 13: SCPI commands
Sample code for PM100A:
Set different measurement parameters
Two different ways to read values
Close VISA session

## Slide 14: Serial COM commands
Each DCs LED driver has a list of commands for the COM interface.
The lists are included in the documentation.

## Slide 15: Serial COM commands
Sample code for DC2100:
COM port has to be known (e.g. device manager)
Open serial port connection
Set connection parameters

## Slide 16: Serial COM commands
Sample code for DC2100:
Operation mode, current, etc. can be set and read out by these commands
Different commands for CC or PWM
Close serial port connection in the end

## Slide 17: Additional information
You can find all the programming documentations and sample codes in this folder: R:\Tech Support\BLU INFOS\Programming
Thank you! Questions?